## Slide 1: WP 1
The Qombs Project is funded by the European Union’s Horizon 2020 research and innovation programme under grant agreement number 820419
Christian Jirauschek
Christian Jirauschek
Johannes Popp
Michael Haider
TUM
Jérôme Faist
Martin Franckie
Giacomo Scalari
Barbara Schneider
Mathieu Bertrand
ETHZ
Mid-term Review meeting
May 13th 2020
Carlo Sirtori
Yanko Todorov
Angela Vasanelli
Azzurra Bigioli
Djamal Gacemi
ENS/CNRS
Augusto Smerzi
Luca Pezzé
Manuel Gessner
CNR

## Slide 2: Content
2
Overview work package 1
Achievements
Work in progress

## Slide 3: WP 1 – Overview
3
Development and application of simulation techniques for investigating carrier transport and noise in QCLs and intersubband detectors
  Conventional numerical simulation methods
  Comparison to cold atom quantum simulations for mutual assessment and improvement
Exploitation of developed methods for the further development of
  QCLs with ultimate goal of “quantum comb” (squeezing/entanglement)
  low-noise intersubband detectors for the characterization of non-classical QCL-combs
Theoretical development of optimal measurement strategies of non-classical comb features

## Slide 4: Gantt chart
4
Month | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36
WP1 - Modeling, numerical simulation and witnesses of squeezing and entanglement |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | M1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | M2 |  |  |  |  |  |  |  |  |  |  |  | 
T1.1- TUM |  |  |  |  |  |  |  |  |  |  |  | D 1.2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
T1.2 - TUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
T1.3 - TUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
T1.4 - TUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | D 1.4 |  |  |  |  |  |  |  |  |  |  |  | 
T1.5 - ETH |  |  |  |  |  | D 1.1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | D 1.3 |  |  |  |  |  |  |  |  |  |  |  | 
T1.6 - TUM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | D 1.5
T1.7 -CNR |  |  |  |  |  |  |  |  |  |  |  | D 1.6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
T1.8 -CNR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
T1.9 -CNR |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | D 1.7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 5: Content
5
Overview work package 1
Achievements
Work in progress

## Slide 6: Deliverable D1.1: First improved QCL comb design (ETHZ/TUM)
6
6
Optimized active region design for improved comb operation, potentially exhibiting enhanced nonclassical features in light emission (see also Task T1.5, Milestone M1).
Goal: Wide and high gain curve, enabling comb operation over an extended bandwidth at high optical power, and thus low noise
Lattice-matched InGaAs/AlInAs/InP to avoid complications from strain
Starting point well-tried QCL structure EV2103, emitting light with high efficiency and power over an extended bandwidth
Two discussion meetings of the TUM and ETHZ groups: 21.2.2019, Munich and 11./12.03.2019, Zürich (with CNR)
Use two independently developed carrier transport simulation tools (Task T1.2) to increase robustness and reliability: NEGF (ETHZ) and EMC (TUM)
Improvements of simulators in terms of speedup, physical modeling and implementation of material parameters
Different optimization routines (e.g., genetic algorithm, Gaussian regression)

## Slide 7: Deliverable D1.1: Carrier transport simulation
7
Monte Carlo (EMC)
(with density matrix corrections)
Ekin
Ekin
Quantum transport
(here: NEGF)
Rate equations
Accuracy
Efficiency

## Slide 8: Deliverable D1.1: Scattering mechanisms
8
Relevant scattering mechanisms in QCLs are evaluated in a self-consistent manner
E
k
Acoustic phonons
Electron-electron
E
k
Optical phonons
E
k
Phonon emission
E
k
Phonon abs.
E
k
Interface roughness
E
k
Impurity
E
k
Alloy disorder

## Slide 9: Deliverable D1.1: Design Goal
Multimode nonclassical states of light (realized by frequency combs)
Envisaged applications:
Quantum networks, relevant e.g. for quantum computation/communication/metrology
H. J. Kimble, Nature 453, 1023 (2008)
9
Wide and high gain curve
High number of states/modes beneficial for applications
Broadband comb
High degree of quantum correlation beneficial for applications
High output power
decreases photon noise
F. Rana et al., PRB 65, 125313 (2002)
Increases four-wave mixing creating multi-mode quantum correlations
C. Reimer et al., Science 351(6278), 1176 (2016)

## Slide 10: Deliverable D1.1: Results
10
Broadband gain at 300 K: Maximize gain integrated over energy range 120-180 meV divided by maximum gain (to suppress high and narrow gain curves)
M. Franckié, J. Popp, M. Haider, C. Jirauschek, and J. Faist, “Numerical optimization of mid-IR QCL frequency combs,” Infrared Terahertz Quantum Workshop (ITQW 2019), Presentation 88, 15-20 Sept. 2019.
Gain (1/cm)
Energy (meV)
40
0
Original structure
150
190
40
110
0
Optimized structure

## Slide 11: Deliverable D1.1: Risk management
Risk: New active region designs cannot be significantly improved over the first generation designs (likelihood: medium)
Has not materialized, as the designs improved with respect to broad and flat gain spectra are significantly better than the original one, showing our simulation and optimization approach is working
The fabricated optimized structure showed broader electroluminescence (more details about fabrication in WP3)
Further optimisations are planned (deliverable D1.3), involving improvement of third-order nonlinearity in active region and of gain bandwidth for 4.5 micron design. We do not expect any increased risks for the future optimizations

## Slide 12: Deliverable D1.2: Improved QCD/QWIP detector designs (TUM/ETHZ/CNRS)
12
Low-noise intersubband detector designs for detecting quantum features in the optical output of QCLs (see Task T1.1). With regard to future commercial applications, we focus on elevated temperatures achievable with moderate effort by thermoelectric cooling, and a wavelength of 4.5 µm where QCLs have the highest output powers.
Quantum cascade detectors (QCDs) vs quantum well infrared detectors (QWIPs)
In discussions between TUM, ETHZ and CNRS, we decided to focus on QCDs
Superior high temperature noise behavior (discussion with ETHZ, CNRS)
Fabrication aspects (discussion with ETHZ)
Established QCL modelling techniques can be adapted

## Slide 13: Deliverable D1.2: Method development
13
Model noise (Task T1.3) as Johnson noise by developing a periodic network model with noise-equivalent conductances
Greatly reduced scattering rates and low upper state occupations impede direct simulation of responsivity/detectivity by ensemble Monte Carlo (stochastic sampling!)
Responsivity/detectivity are calculated from simulated intersubband scattering rates and absorption spectrum, rather than directly extracted from simulations of irradiated detector
  Use artificially increased level occupations for improved scattering statistics
  Use relations of thermodynamic equilibrium valid for non-irradiated QCD structure

## Slide 14: Deliverable D1.2: Method validation
14
Test structure N1022 (4.7 µm)
Position [nm]
-240
-220
-200
-180
-160
0
100
200
300
400
500
Energy [meV]
1/Temperature [1/1000K]
2
3
4
5
6
7
8
9
10
Simulation
Experiment
No deviation from Arrhenius line at low T in simulation
Resistance [cm2]
100
150
200
250
300
0
2
4
6
8
10
Responsivity [mA/W]
J. Popp, M. Haider, M. Franckié, J. Faist, and C. Jirauschek, “Monte Carlo modeling of terahertz quantum cascade detectors,” URSI GASS, accepted (http://arxiv.org/abs/2004.05891).
THz test structure (84 µm, 10 K)
Position [nm]
0
40
80
120
160
Energy [meV]
0
200
Wavenumber [1/cm]
100
90
100
110
120
130
140
150
160
Responsivity [mA/W]
0
2
4
6
8
10
Exp.
Sim.
Temperature [K]

## Slide 15: Deliverable D1.2: QCD optimization (CNRS designs)
15
Position [nm]
-180
-170
-160
-150
-140
-130
0
0.2
0.4
Position [nm]
-160
-150
-140
-130
-120
Energy [eV]
Frequency [THz]
55
60
65
70
75
0
2
4
6
8
10
QCD 1
QCD 2
Responsivity [mA/W]
Simulation of original (left) and improved (right) design at 280 K
Predicts similar responsivities
Predicts factor 50% higher detectivity (2.92x107 vs 2.07x107 Jones) of improved QCD due to higher resistance

## Slide 16: Deliverable D1.2: Brute-force optimization
16
Original design by CNRS
Hilbert curve centered on original design
Energy [eV]
Maximum detectivity
Well 3
Barrier 2-3
Well 2
0
100
200
300
400
500
Position [nm]
0
0.1
0.2
0.3
0.4
0.5
0.6
2
3
4
5
7
1'
1
6

## Slide 17: Deliverable D1.2: Optimization with Gaussian process regression
Start design N1022 (4.7 µm)
17
0
100
200
300
400
500
4
2
0
2
4
x108
Position [nm]
-240
-220
-200
-180
-160
0
100
200
300
400
500
Energy [meV]
Detectivity [Jones]
Simulated specific detectivities
Hilbert curve node number
95% prediction interval
Mean
Training data
N1022
Optimized
J. Popp, M. Haider, M. Franckié, J. Faist, and C. Jirauschek, “Numerical optimization of quantum cascade
detector deterostructures,” NUDOD 2020, accepted.

## Slide 18: Deliverable D1.6: Coefficient to quantify number squeezing in multi-mode systems (CNR)
18
Theoretical development of optimal measurement strategies for detection and quantification of squeezing in the optical QCL output, which is impeded by low detection efficiencies <60% in the mid-infrared range (see also Tasks T1.7 and T1.8).
Standard balanced homodyne detection of squeezing does not work well due to
limited efficiencies of mid-infrared detectors
elevated output powers of QCLs which impedes finding a strong local oscillator
Squeezed signal
Local oscillator
Photodetector
Beam splitter
Spectrum analyzer
-/+

## Slide 19: Deliverable D1.6: Developed strategies
19
Homodyne cross-correlation
Works with weak local oscillator
Correlation measurement not effected by losses
Squeezed signal
Local oscillator
Photodetector
Beam splitter
Correlator
Self-homodyne detection
Does not need external local oscillator
Also suitable for multimode systems
Squeezed signal
Photodetector
Beam splitter
Cavity
-/+

## Slide 20: Deliverable D1.7: Criterion for the identification of multimode entanglement in QCLs (CNR)
20
Theoretical development of optimal measurement strategies for detection and quantification of multiparameter squeezing and multimode entanglement in QCL combs (see also Task T1.9).
Spin-squeezing matrix:
Generalization of spin-squeezing coefficient to multiparameter settings
Provides experimentally feasible witness for multimode entanglement/squeezing
Violation of resulting matrix inequality signals multiparameter squeezing, implying multimode entanglement
Reveals optimal strategies for the design and analysis of the photonic experiments
Full characterization of entanglement requires full knowledge of system density matrix (generally not experimentally accessible)
Often interested in entanglement relevant for specific purposes (e.g., sub-shot-noise interferometry)

## Slide 21: Content
21
Overview work package 1
Achievements
Work in progress

## Slide 22: Deliverable D1.3: Second generation QCL-comb active region design (M24)
22
Improving QCL comb designs
Better combs:
Increase width and flatness of gain spectrum
Design spectrally flat group velocity dispersion from active region
Optimize for 4.5 micron QCL
Improve squeezing/entanglement:
Optimize χ(3) of the active region to increase four-wave mixing
Injection barrier
Lasing
LO phonons
χ(3)
Lasing mode
Gain
Martin Franckie (ETHZ) visit to CNR-INO/LENS in Dec. 2019
How to quantify and improve squeezing / χ(3)?
How to study the effect of gain and loss on entanglement?
Suggestion for cleaner system:
Only two side-bands (instead of many comb lines)
Alternative: externally pumped χ(3) medium
Cold atom counter-part (Rb atoms simulate photons)
Photons  occupations of spin states in atomic cloud
Nonlinearity χ(3)  simulated by atom collisions
Gain/loss  simulated by laser mediated transitions

## Slide 23: Deliverable D1.4: Open-source code for dynamic QCL simulations with noise (M24)
In progress (see also tasks T1.3 and T1.4):
Add spatiotemporal noise sources
Add chromatic dispersion and diffusion (for spatial hole burning)
Add microwave transmission line dynamics for including microwave-optical coupling
Planned collaboration stay of Mathieu Bertrand from ETH at TUM for 2 weeks
Review paper: C. Jirauschek et al., “Optoelectronic device simulations based on macroscopic Maxwell-Bloch equations”, Adv. Theory Simul. 2, 1900018 (2019).
23
Typically, Maxwell-Bloch equations are treated in RWA/SVAA
  Computationally efficient due to coarser spatiotemporal grid
  Only valid for relatively narrowband (and not too strong) optical fields
Meanwhile octave-spanning QCLs: M. Rösch et al., Nat. Photon. 9, 42 (2015)
Full-wave Maxwell-Bloch equations
Open-source project mbsolve (TUM): https://github.com/mriesch-tum/mbsolve
Description of mbsolve: M. Riesch and C. Jirauschek, https://arxiv.org/abs/2005.05412
  Multi-level simulations beyond the common two-level approximation
  Numerical efficiency, long-term stability, preservation of important physical properties
  Computational speedup by using parallelization techniques (OpenMP, CUDA, ...)

## Slide 24: Deliverable D1.4: First comb simulations with mbsolve
24
3.1
3.2
3.3
3.4
3.5
3.6
3.7
3.8
3.9
4
4.1
Frequency [THz]
10-4
10-2
100
Position [nm]
100
50
0
0
0.05
0.1
0.15
Energy [eV]
Tunneling
Coh. light-matter coupling
Scattering
Design: D. Burghoff et al., Nat. Photon. 8, 462 (2014)
Power spectrum [arb. u.]